## Slide 1: Mechanisms – 4/12/24
Keith, Elijah, Anna, AJ

## Slide 2: Weekly Goals Assessment
Past week’s achievements:
  Discussed motor selection (Axial Flux Halbach BLDC)
General Goals:
  Battle royal Ws
  pluh
Individual Goals:
  We’re all doing the motor 

## Slide 3: Team Accomplishments – Motor selection
Axial Flux
  PRO – More Torque
  PRO – High Power/Volume Ratio
  CON – Lower Cap on RMP (Nominal)
Outboard Hub Mounting
  PRO – No Transmission = Low Complexity
  CON – No Transmission = No Gear Speed Selection
    Mitigated by electric motor torque characteristics
Halbach Array Configuration
  PRO – No Back-Iron
    Saves weight; especially important if hub mounted (un-sprung)
    Typically used to direct magnetic field towards the rotor to assist in crossing airgap.
  CON – Harder to source most efficient shape
  Less Pole Rotations
3 Phase BLDC (Brushless Direct Current)
  PRO – Brushless = No kinetic friction losses and longer lifespan
  PRO – Direct Current is already what the batteries supply
  PRO – 3 Phase is a common setup
  CON – Brushless = Electronically controlled (lil more work for electrical)
More info in #reference-material-me

## Slide 4: Next Week’s Goals
Continue research examining motor design specifications
  Find sources for magnets
    Equations specify dimensions for optimal efficiency
    May have to cut them ourselves
  Compare other sources for copper winding (other than McMaster Carr)
  MAYBE start initial design work (def not idk why I wrote that)
  Uhh
  Idk the meeting is starting…